## Slide 1
Collision avoidance and coordination for a fleet of robots
Luca Marseglia
Amazon Robotics machines in a Amazon warehouse

## Slide 2
Background: Centralized approaches
2024 October | Slide 2
A central controller manages the movements of all the robots in the system
Benefit from their global optimality, as the entire system’s configuration is considered while taking decisions
Poorly scalable
Typically used in offline planning scenarios

## Slide 3
Background: Decentralized approaches
2024 October | Slide 3
Distribute the responsibility for collision avoidance across the robots
Usually used in real-time applications
Highly scalable
Struggle with sub-optimality

## Slide 4
Chosen approach: MINLP + GA
2024 October | Slide 4
The problem will be formulated as a MINLP optimization problem
The optimization problem will be solved using GA
MINLP is suitable for modelling a complex problem that involves both continuous and integer variables as well as nonlinear constraints
GA is suitable for solving multi-dimensional optimization problems without relying on gradient information, because uses a population based approach, as exact gradients can be challenging to compute
Furthermore, is flexible in managing multiple objectives (in this case time and energy)
This approach can offer a good level of optimality compared to online and centralized methods

## Slide 5
Introduction
2024 October | Slide 5
System of robots
With paths produced through the CDT-RRT*
With trajectories associated to each of the n paths
Kinematic constraints: velocity and acceleration
Definition of collision between any two robots:

## Slide 6
Problem statement
2024 October | Slide 6
The algorithm must ensure that the robots respect the safety margin during their movement by modifying their velocities based on their kinematic constraints.
The optimization must balance multiple objectives, including:
  Minimizing total travel time
  Minimizing energy consumption
  Ensuring a safety margin between the robots during motion

## Slide 7
Trajectory generation
2024 October | Slide 7
Continuous function
First derivative is not continuous
Continuous function
First and second derivative are also continuous
Too much overshooting
Continuous function
First derivative continuous
Second derivative is not continuous
Avoids overshooting

## Slide 8
Trajectory generation
2024 October | Slide 8

## Slide 9
Proposed approaches
2024 October | Slide 9
Brute-force approach
Prioritized planning
Optimization approach (MINLP + GA)
  Maximum velocities
  Slow-down segment
  Multi-objective (time+energy)

## Slide 10
Brute-force
2024 October | Slide 10
Get all the possible combinations of maximum velocities
Find the best collision-free combination among them
Can use a minimum velocity to decrease significantly the number of combinations:
The criteria for choosing the best velocity combination is the minimization of:

## Slide 11
Prioritized planning
2024 October | Slide 11
Plan trajectories starting from the robot with the highest priority at maximum velocity
Plan the remaining trajectories by scaling the maximum velocity to avoid collision with the robots with higher priority
Very fast execution times but poor results based on the choice of the heuristics

## Slide 12
Optimization approach: MINLP + GA
Maximum velocities optimization
2024 October | Slide 12
To overcome the limitations of the brute-force approach and prioritize planning, an approach that directly optimizes the maximum velocities of each robot’s trajectory was implemented
The optimization objective is to minimize the total travel time, which is defined as the time taken for the last robot to reach the goal. At the same time, collision avoidance is guaranteed by setting constraints that prevent robots from occupying the same space at the same time.

## Slide 13
Optimization approach: MINLP + GA
Slow-down segment optimization
2024 October | Slide 13
This method focuses on strategically slowing down robots only during the initial part of their paths to prevent collisions, while allowing them to operate at their maximum allowable velocities for the rest of their trajectories

## Slide 14
Optimization approach: MINLP + GA
Multi-objective optimization
2024 October | Slide 14
Natural trade-off: optimizing for speed tends to increase energy consumption, while optimizing for energy efficiency tends to lengthen the completion time.
f1
f2

## Slide 15
Simulation results:
Brute-force approach

## Slide 16
Simulation results:
Prioritized planning

## Slide 17
Simulation results:
Slow-down segment - Effect on the trajectories

## Slide 18
Simulation results:
Slow-down segment – Parameters selection
Population size: 100

## Slide 19
Simulation results:
Slow-down segment – Parameters selection

## Slide 20
Simulation results:
Slow-down segment – Population size selection

## Slide 21
Simulation results:
Slow-down segment – Population size selection

## Slide 22
Simulation results:
Slow-down segment – Population size selection

## Slide 23
Simulation results:
Maximum velocities – Parameters selection
Population size: 100
Mutation: Uniform

## Slide 24
Simulation results:
Maximum velocities – Parameters selection
Population size: 100 Mutation: Self-adaptive

## Slide 25
Simulation results:
Maximum velocities – Parameters selection
Population size: 1000 Mutation: Self-adaptive

## Slide 26
Future work
Add the simulation results of the maximum velocities approach to the report
Produce simulations with the constraint offset for the slow-down segment approach
Produce and analyze simulations for the multi-objective optimization