## Slide 1
Collision avoidance and coordination for a fleet of robots
Luca Marseglia
Amazon Robotics machines in a Amazon warehouse

## Slide 2
Summary
2024 August | Slide 2
Context
Algorithm
Issues & Future work

## Slide 3
Modified CDT-RRT*
2024 August | Slide 3
First, the CDT-RRT* has been modified to only choose the sample points in the middle of the edges.

## Slide 4
Context
2024 August | Slide 4
The goal is to avoid collisions between robots at the end of their path, when they start to follow common trajectories, in a coordinated fashion.
The previous approach aimed at changing the maximum velocity of the robots along the whole path to achieve this task.

## Slide 5
Simple case
2024 August | Slide 5
But the previous approach had some drawbacks.
For this reason, the current approach aims at changing only the velocity of the robots in the segments that are involved in the collisions.
In particular, for this time, only collisions in the last segments are solved.

## Slide 6
Simple case
2024 August | Slide 6
Starting from the simplest case with two robots, the idea of the algorithm is to slow down the robot that is further from the goal at the instant of the collision (in this case, the blue robot).
This is because, if the opposite is done, in most of the cases collision becomes unavoidable.

## Slide 7
Collisions between 5 robots
2024 August | Slide 7
Let’s now consider a more complex situation.
In this case, all the robot have a similar finish time, that is:
Finish times:

## Slide 8
The algorithm iteratively looks for the furthest robot among the collisions and increases its travel time by 1 for that segment.
increasedTimes = 1 0 0 0 0
increasedTimes = 1 0 1 0 0
increasedTimes = 2 0 1 0 0
increasedTimes = 2 0 2 0 0
increasedTimes = 3 0 2 0 0
[…]
Steps
2024 August | Slide 8

## Slide 9
Without collisions
2024 August | Slide 9
Finish times:

## Slide 10
Issues & Future work
2024 September | Slide 10
This algorithm doesn’t work for the other segments different from the last one.
Or, at least, a similar version could be developed for them.

## Slide 11
Issues & Future work
2024 September | Slide 11
But the problem might not be so immediate, because if the velocity of a robot is changed only for a segment, this change could generate new collisions with other intersecting segments.